## Slide 1
DrainLens
Stormwater flood risk for residents of Greater Melbourne communities that flood repeatedly.
Pre-deployment check · Team TA28 · FIT5120 S2 2026
Tuesday 1 September 2026
Notes: Frame the session: we would rather be asked how it works than shown that it runs. Everything in this deck is measured and can be opened in the editor.

## Slide 2
THE SYSTEM IN SIXTY SECONDS
Three parts, one of them deliberately absent
1
Offline Python pipeline
Reads a photogrammetric point cloud and the council’s drainage records. Produces a small set of static, versioned artefacts. Never deployed — it runs on a laptop.
2
Browser application
React + TypeScript + Vite. Loads those artefacts and draws them on a canvas. No map library: the extent is already projected into metres.
3
Scenario engine
A separate TypeScript package with no DOM. Routes water over the terrain inside a Web Worker and returns a comparison, never an absolute depth.
There is no application server in Iteration 1 — and that is a decision, not a gap.
Notes: Say the last line out loud. It invites the question we have a good answer to, instead of letting it arrive as an accusation.

## Slide 3
ARCHITECTURE
Build-time heavy, runtime thin
OFFLINE · PYTHON
pipeline/
LiDAR → bare earth (SMRF)
depressions, D8 routing
map geometry, trace
scene packing
STATIC FILES · PLAIN GET
Artefacts
map.json 318 KB
derived.json 183 KB
trace.json 37 KB
addresses.json 3 KB
scene/*.bin 1.28 MB
THE ONLY THING DEPLOYED
apps/web
canvas map
address search (in memory)
downstream trace
engine in a Web Worker
Why nothing runs on a server
A resident can search an address, follow the drainage, run a blockage comparison and read the result — without one request that says anything about them. That is AD1, no identity. The cheapest way to keep a promise about data is never to receive it: a search box that calls a server sends every keystroke of somebody’s home address to it, and a log line is storage.
Notes: If asked why not build a backend anyway: serving static artefacts is static hosting behind a CDN, not an application. Building endpoints against a contract nobody is calling is how a system acquires surface area it then has to defend.

## Slide 4
DATA FLOW
One click, end to end
The standard question is “trace a request”. We have no requests — so here is the same journey across a thread boundary instead of a network one. Same files, same functions, same logic, same return path.
1
ScenarioSetup.tsx
The Run button
2
App.tsx · cellOf()
Pit → grid cell index
3
session.ts · reduce()
comparison-started
4
useScenario.ts · run()
Request id, postMessage
5
worker.ts · handle()
Off the main thread
6
engine.ts · runScenario()
Sufficiency gate, then solve
7
engine.ts · solvePosition()
Twice: scenario + baseline
8
checks.ts · checkMassBalance()
Water must be conserved
9
Result.tsx + outcome.ts
Wording chosen from the outcome
Why a Web Worker: a million cells, solved twice per rainfall position. On the main thread the map freezes mid-gesture — and a frozen map reads as a crash, so the person taps again and now two runs compete.
Notes: Requests carry an id and replies are matched against the newest, so changing the blockage mid-run shows the answer to what was asked last, not whichever finished second.

## Slide 5
HOW WE JUSTIFY A NUMBER
Measured, not chosen
Every parameter in the terrain pipeline was set by measuring its marginal effect and stopping at the knee — not by taking a paper’s default.
26 m
Ground-filter window.
12→18 m removes 5.8 ha more,
18→26 m a further 2.2 ha,
then ~1 ha per step — which is
terrain being shaved, not
buildings being found.
0.25 m
Depression floor.
Two independent arguments
land on it: the knee in the
volume curve, and the source’s
own quoted accuracy.
1 m
Simplification tolerance.
Set by what can be seen, not
by the cell size. 0.25 m kept
every lattice staircase corner:
40,490 vertices → 10,986.
The cross-check
92.2%
of council building footprints were independently removed by our ground filter — a 2020 vector dataset and a morphological filter over a 2018 cloud, agreeing with nothing in common but the ground.
The reverse holds at only 51.9% — half of what the filter removes is tree canopy, and water flows under trees.
That asymmetry is the measured reason the filter’s object mask cannot serve as flow barriers — and it is why we fetch the footprints separately.
Notes: The filter’s one predicted blind spot was confirmed at the predicted threshold: 44.7% missed beyond 13 m inside a roof, and a 26 m window reaches 13 m in. Predicted from theory, pinned by a synthetic test, confirmed on real ground.

## Slide 6
THE DEFECT STORY WORTH TELLING
Closing the mass balance
A check in the engine asserts that rain in equals captured + ponded + left-the-window. It found three separate bugs in sequence.
1
The pipeline shipped the raw surface while the flow field came from the conditioned one — water routed by one terrain, stored by another.
2
Ordering cells by elevation is only a proxy for topological order. 509 cells in a million were exactly level at float32, so water solved out of sequence. Replaced with Kahn’s algorithm.
3
Depressions resolved in one pass ordered by rim height stranded water in already-resolved stores — a deep pit in low ground can have a higher rim than the hollow feeding it. Passes now repeat until nothing moves.
WATER LOST
71.55%
before
0.00%
after
None of the three was visible in the output. Every one produced a map that rendered, panned and looked entirely plausible.
Notes: This is the best answer we have to “do you understand your own code”. Be ready to explain why elevation ordering is only a proxy, and why Kahn’s is exact by construction on a flow field.

## Slide 7
US 1.2 · BUILT 29 AUGUST
Two kinds of nothing
The browser could trace the drainage from map.json alone — every pipe already carries an upstream and a downstream pit. It cannot do one thing, and that is why there is a pipeline stage for this.
7
leaves the mapped area
The council recorded where the pipe goes, and it goes somewhere we clipped off. The path continues — we are simply not drawing it.
29
destination never recorded
The council never recorded where the pipe goes. The path stops, because the record stops.
Both look identical in map.json.
Presenting all 36 as “the pipe goes nowhere” would state something false about the source data — which is exactly what AC 1.2.2.d exists to prevent. Only the council-wide graph knows which is which, so we resolve it once, offline, into a 37 KB artefact and ship the reason with every link.
Notes: Direction is read from the topology, not the vertex order — the export orders vertices however the surveyor captured them, so trusting them gives arrows right about half the time.

## Slide 8
THE FINDING TO VOLUNTEER
There are no recorded outlets
215
pits in the extent with no downstream pipe
83
of those are kerbside inlets
0
outfalls, endwalls or discharge points
A kerbside grate is not where a drainage system ends.
It is where the record does.
AC 1.2.2.c offers “the recorded outlet or the last known connection”. In this data it is always the second — so neither the artefact nor the traversal has an outlet termination to return, and a test asserts the word never appears in the wording a resident reads. A trace announcing an outlet would be inventing the end of a drainage system.
Notes: Volunteering a limitation reads as understanding. Being caught by it reads as not knowing.

## Slide 9
DESIGN POSITION
The distinctions are types, not conventions
No clear change is not Insufficient information
The first means the calculation ran and found no difference. The second means it could not be made. A resident acting on the first is being reasonable; a resident acting on the second, believing it was the first, is acting on nothing. Different branches of the outcome union.
A blockage setting is not a visible condition
One is an assumption a person chooses for a scenario; the other is what a photograph shows. There is deliberately no function anywhere converting between them, and a test asserts none appears.
A network limitation is not an insufficiency
Where a pipe leads has no bearing on the surface calculation, so a missing downstream connection travels alongside a successful result rather than replacing it.
Every displayed value also carries a basis — sourceProvided, derived, assumed or inferred. It is not optional: a value that cannot say where it came from has no constructible shape.
Notes: Four insufficiency reasons, each with its own distinct action: terrain_unavailable, invalid_inlet, scenario_calculation_failed, comparison_not_comparable.

## Slide 10
SCOPE
58 of 77 acceptance criteria met
Every box checked against the code on 29 August, not assumed from a task list.
Chart: 
| US 1.1 Explore | US 1.2 Trace | US 1.3 Cross-section | US 2.1 Set up | US 2.2 Compare | US 2.3 Understand
Met | 17 | 9 | 0 | 12 | 12 | 8
Not met | 4 | 0 | 8 | 0 | 5 | 2
The nineteen that are not
The cross-section (US 1.3) is not built — eight criteria.
The map does not mark or centre on the selected address; it reaches the panel text and stops. Two criteria, and the smallest real hole.
No rainfall control on the result screen — four. The engine already solves three positions per run, so this is interface work.
The result does not visually separate recorded from derived from assumed — two. The map already does.
The result map drops the selected pit and its path — one.
No terrain layer control, no plain-English water explanation — two.
An unticked box that might mean “not built” or might mean “nobody looked” is worth nothing to a reviewer — so each one now names its reason.
Notes: US 1.3 was always the most likely to drop: pit depth is missing for 95.4% of the record and the surviving fraction is internally inconsistent, so most of the work is the unavailable state rather than the drawing.

## Slide 11
HOW IT WAS BUILT
Development process
PR
Pull requests
7 opened, 6 merged, each with written technical review. Zero direct pushes to main — enforced by a GitHub ruleset and tested by attempting one.
CI
Continuous integration
Typecheck, tests and coverage on every PR, Node and Python jobs. npm ci rather than npm install, so lockfile drift fails the build.
TS
Tests
334 TypeScript across 16 files, 332 Python. Written before or alongside every judgement-carrying component.
%
Coverage
91.17% Node, 91.44% Python — both above the 88% floor, with packages/schema and packages/scenario held to 90% separately.
⌘
Branching
main ← develop ← feature branches, held throughout. Commit messages explain why, not what.
◆
Artefacts
Full-size intermediates git-ignored; the clipped published copies committed, so the frontend runs from a clone with no Python toolchain.
Outside the repository and still to confirm: the peer-programming observation document, the PGP iteration build folder, two structured desk checks, and the LeanKit board. The gates table records these as unmet rather than assumed.
Notes: Be candid here — the gates table in ITERATION-1-TASKS.md has four rows with an em dash where a status should be, and a mentor reading it will see the same gaps.

## Slide 12
MEASURED 29 AUGUST
Where we hold the line, and where we do not
✓
Coverage, overall
≥ 88%
91.17% Node · 91.44% Python
✓
Coverage, judgement-carrying modules
≥ 90%
schema and scenario, enforced separately
✓
Merges via pull request with review
100%
enforced by ruleset
✓
Direct pushes to main
zero
enforced, and tested by attempting one
✓
Node suite runtime
< 5 s
1.4 s
✗
Python suite runtime
< 5 s
88 s
We are raising this rather than being shown it
One test is 32.7 s of the 88 — a 20,000-vertex zigzag through Douglas–Peucker, that algorithm’s pathological worst case. It exists to prove simplify() iterates rather than recurses, and Python’s recursion limit is 1,000, so a path a twentieth as long would prove the same thing. Another ~45 s is test_terrain.py building real grids. Neither is a product defect, and CI blocks on the Node suite — but a rule quietly exempted for the slow half is not a rule.
Notes: The old README claimed 100% Node and 99% Python with suites around a second. That was stale and flattering; it was corrected on 29 August.

## Slide 13
OPEN DECISION · WE WOULD VALUE YOUR VIEW
The network is redundant under our assumption
With the mass balance closed, blocking any single inlet produces no visible difference at any rainfall from 20 to 200 mm.
This is not a bug. The median inlet captures only its own cell’s rain, and every drain downstream takes 60% of whatever reaches it — so water released by one blocked inlet is absorbed within a few cells. That 60% is an assumed capture fraction standing in for inlet geometry, grate condition and approach flow, none of which the source data records.
A
Lower the capture fraction
Makes a single blockage visible, but the number becomes one we chose to produce an effect rather than one we can defend.
B
Block several pits at once
Defensible and closer to how a street actually floods. Costs interface work in the setup screen.
C
Report two bands and say why
Honest and cheap. The demonstration then shows a comparison that mostly returns “no clear change”.
We lean towards B. It decides what the demonstration can show, so it is the one decision we would rather make with you than after you.
Notes: The task list reserved this question from the start: the capture fraction’s sensitivity decides whether the interface may report three comparison bands or two.

## Slide 14
OVER TO THE SCREEN
What we will show you live
1
Search 46 Gatehouse Drive
Resolved in the browser against a shipped index. Nothing leaves the tab.
2
Follow water and drainage
Surface-water paths and pits on by default; everything else in a collapsed section.
3
Select pit 1145091 and follow it
33 recorded pipes, 15 steps downstream, stopping in five places for three different reasons.
4
Set up and run a comparison
Blockage unselected until chosen, rainfall in millimetres, both labelled as assumptions.
5
An insufficient-information state
Named reason, distinct action, and no placeholder result beside it.
Ask us to open any file.
The three most worth opening are engine.ts for the water model, viewport.ts for the one place the map flips north to canvas-y, and ground.py for the filter we wrote because PDAL would not install.
Notes: Everyone on the team should be able to give the sixty-second system answer and the no-backend answer without notes. Those two get asked regardless of who wrote what.